## Slide 1: Software Defined Networks: Overview
CS6393
Lecture 9-1

## Slide 2
Traditional Networks

## Slide 3: Overview of Traditional Networks Architecture
Infrastructure Layer
Management Layer
Control plane
Data plane
Command Line Interface (CLI)
Traditional Network
Configuration commands
Network engineer

## Slide 4: Network Devices in Traditional Networks
  Vendor-specific and heterogeneous.
  Requires manually configuration.
    Costly.
    High-rate of configuration errors.
    Serious security breaches even for well-known security guidelines.
  Hardwired with specific algorithms and protocols to route, control and monitor data flow.

## Slide 5: Problems in Traditional Networks
Lack of global visibility of the network state.
Difficulties in deploying and maintaining coherent network-wide policies.
Innovation in networking functionalities and control is difficult.
Unmanageable and high operational cost by network engineers.
Complex and weak integration of decentralized networking devices.
Hard to maintain stable and robust network security.

## Slide 6: Security Policies in Traditional Networks
Traditional networks lack security automation and run-time deployment of security policies.
Lack for runtime update of security policies in response to traffic behavior or intrusions.
To implement security policies, network operators need to
  Translate high-level security policies into low-level configuration commands.
  Implement low-level commands manually into large sets of vendor-specific devices.
Updating security policies might require changing the hardware or updating its firmware.

## Slide 7
Software Defined Networks

## Slide 8: Software Defined Networks (SDN)
SDN decouples the network control from the data forwarding plane in routers and switches.
The result:
  Control plane (logically centralized).
  Forwarding plane takes decisions from the control plane.
  Applications and services are implemented on top of the control Plane.
    Control plan maps the entire network to the application layer.
  Programmability of network functions and control.
Control plane
Data plane
Decoupling
SDN idea
Control plane
Data plane
Decoupling
Legacy switch
Legacy router

## Slide 9: Decoupling : The Idea behind SDNs
Software Defined Networks
(Centralized)
Control plane
(Distributed)
Data plane
Decoupling
Dumb, fast
Smart
OpenFlow
Protocol
OpenFlow-enabled device
OpenFlow Controller
OpenFlow
  A Protocol between the control plan and data plane.
  Describes how controller and a network forwarding device should communicate.
Notes: Comment conteralized
distributed

## Slide 10: Network Programmability
Control plane
Data plane
Southbound Protocol
(OpenFlow)
Northbound APIs
Network
Applications
Application plane
Abstract
view
  Network Programming Interface
  Traffic mgmt.

## Slide 11: The three Planes of SDN Architecture
Application Plane: SDN applications for various functionalities, such as
  network management
  traffic automation
  network Monitoring
  security services.
  etc.
Control Plane: Logically centralized control framework that:
  runs the Network Operating System (NOS)
  maintains global view of the network.
  provides hardware abstractions to SDN applications.
Data Plane: Forwarding elements that:
  forward traffic flows based on instructions from the control plane.

## Slide 12: Overview of SDN Architecture
Topology Service | Entry Pushing
Routing Service | Device Management
Statistics Collection | Link Discovery
Switch Management | Other
Routing
Firewall
Load
Balancing
Intrusion Prevention
Network Visualization
Other
. . .
Applications
Network APIs
Network Services
Virtual Network Resources
Controller
OpenFlow Protocol
Infrastructure
Switches
VLANs
Links
Ports
Config- urations
Traffic payloads
Statistics
Other
Topology
Hosts
Devices
Flow tables
Manage
Decoupling
Control plane
Data plane
Flow table
Open Interface: needs control

## Slide 13: Enhanced Network Security in SDN
Network security is enhanced in SDN via:
  Network programmability.
  Centralized control of network behavior.
  Global visibility of the network state.
    Easier to spot network vulnerabilities and intrusions.
    Easier to implement security policies.
    Easier to mitigate the risks of policy collision.
  Run-time implementation of security policies.
  Run-time manipulation of traffic forwarding rules.
  Software based implementation of security policy.
    No hardware change or firmware update needed.

## Slide 14: Flow Table Structure
match fields: to match against packets.
actions: to be applied for the matching packet/flow.
priority: precedence of the flow entry.
counters: updated when packets are matched.
timeouts: maximum time/idle time before flow is expired by the switch.
Match Fields | actions | priority | Counters | Timeouts | …
Packet
from network
Parse header fields
Match Found?
Update counters
Send to controller
Yes
No
Apply actions
Packet Processing in OpenFlow Switch

## Slide 15: Flow Table Structure example flow rules
MAC src | MAC dst | IP src | IP dst | TCP port src | TCP port dst | Priority | Action | Packets
..:00:01 | ..:00:04 | * | * | * | * |  | Port-4 | 
..:00:04 | ..:00:01 |  |  |  |  |  | Port-1 | 
* | * | * | 10.0.0.3 | * | * |  | Drop | 
Port-2
Port-3
Port-4
Port-1
OpenFlow Table entry |  | Rule | Priority | Action | Counters
Host-A
MAC: 00:00:00:00:00:01
IP: 10.0.0.1
Host-D
MAC: 00:00:00:00:00:04
IP: 10.0.0.4
Host-B
MAC: 00:00:00:00:00:02
IP: 10.0.0.2
Host-C
MAC: 00:00:00:00:00:03
IP: 10.0.0.3
SDN Controller
OpenFlow Switch
Flow tables
Packet
from network
Parse header fields
Match Found?
Update counters
Send to controller
Yes
No
Apply actions
Packet Processing in OpenFlow Switch
…

## Slide 16: Flow Rule Insertion Example - Routing app
Routing app
Host-A
Host-B
Host-D
1
2
3
Parse packet
Read topology info.
Insert flow rule
Insert flow rule:
Mac-Host-A -> Mac-Host-D: Port-4
4
5
8
9
Switch receives a network packet
If a matching rule found in table, apply actions;
otherwise, forward packet to controller.
Forward packet to network apps
Find shortest path
6
Read hosts info.
7
Flow rule:
Mac-Host-A -> Mac-Host-D : Port-4
Controller
Port-4
Port-1
Port-2
Packet
from network
Parse header fields
Match Found?
Update counters
Send to controller
Yes
No
Apply actions
Packet Processing in OpenFlow Switch
Host-C
Port-3

## Slide 17: Flow Rule Insertion Example - Firewall app
Firewall
app
SDN
Controller
Host-A
Host-B
Host-C
1
2
3
Parse packet
Check security policy
Security Policy:
Deny connections from Host-A to Host-C.
Allow connections from Host-B to Host-C.
Enforce security policy
Insert flow rule: Host-A -> Host-C: Drop
4
5
6
8
Switch receives a network packet
If no matching rule in switch, forward packet to controller
Forward packet to network apps
Host-A -> Host-C: Drop
Decision to controller
7

## Slide 18
SDN Security Challenges

## Slide 19
Apparent Control Plane Security Challenges
DoS Attacks
Threats due to Scalability
Challenges in Distributed Control Plane
  -SDN response times
  -IP packets with random headers
  -Huge # flow rules
  - Information aggregation from multiple domains.
  - different privacy rules in different domains.
19
© Abdullah Al-Alaj
Ahmad, Ijaz, Suneth Namal, Mika Ylianttila, and Andrei Gurtov. "Security in software defined networks: A survey." IEEE Communications Surveys & Tutorials 17, no. 4 (2015): 2317-2346.

## Slide 20: Application Plane Security Challenges
Lack of access control for SDN apps
Lack of authentication mechanisms for SDN apps
Fraudulent and contradicting flow rule insertion
  Requires a permission system to apply least privilege on apps
  Requires a flow rule conflict resolution
  Requires a trust relationship between the
  controller and apps
20
© Abdullah Al-Alaj
Ahmad, Ijaz, Suneth Namal, Mika Ylianttila, and Andrei Gurtov. "Security in software defined networks: A survey." IEEE Communications Surveys & Tutorials 17, no. 4 (2015): 2317-2346.

## Slide 21: Contradicting flow rule insertion - example
Server-2
Security App
Load Balancer
Other App
…
Host-1
Host-2
Host-n
…
Server-1
Server-m
1
2
3
4
5
6
 |  | In port | MAC src | MAC dst | VLAN ID | IP src | IP dst | TCP psrc | TCP pdst | Priority | Action
Rule1 |  | * | * | MAC Server-2 | 10 | * | * | * | * | 150 | drop
Rule2 |  | * | MAC Server-2 | * | 10 | * | * | * | * | 150 | drop
Rule3 |  | 1 | MAC Host-1 | MAC Server-2 | 10 | * | * | * | * | 200 | out port =5
Rule4 |  | 5 | MAC Server-2 | MAC Host-1 | 10 | * | * | * | * | 200 | out port =1
 |  | … | … | … | … | … | … | … | … | … | …
Assume this sequence of activities by SDN Apps.
Security App has identified Server-2 as Malicious server.
Security App Inserts rule1 & rule2 to quarantine the flows to/from Server-2.
Server-2 becomes least loaded server in the pool.
Load Balancer App Inserts flow Rules rule3 & rule4 to redirect traffic to Server-2.
Load Balancer App violates the security policy implemented by Security App.
21
Al-Alaj, Abdullah, Ravi Sandhu, and Ram Krishnan. "A Formal Access Control Model for SE-Floodlight Controller." Proceedings of the ACM International Workshop on Security in Software Defined Networks & Network Function Virtualization. ACM, 2019.

## Slide 22: References
Ahmad, Ijaz, Suneth Namal, Mika Ylianttila, and Andrei Gurtov. "Security in software defined networks: A survey." IEEE Communications Surveys & Tutorials 17, no. 4 (2015): 2317-2346.
Al-Alaj, Abdullah, Ravi Sandhu, and Ram Krishnan. "A Formal Access Control Model for SE-Floodlight Controller." Proceedings of the ACM International Workshop on Security in Software Defined Networks & Network Function Virtualization. ACM, 2019.